## Slide 1: GridLAB-D Tutorial 4
David P. Chassin
Summer 2016
dchassin@stanford.edu
All registered trademarks are hereby recognized.
Part 1: Demand response

## Slide 2: Tutorial Overview
Demand Response
  Background on Demand Response (DR)
  Implementation of DR
  Modeling of DR in GridLAB-D
Retail Markets
  Tariff implementations
  Real-time pricing by retail auctions
Database operations
  MySQL databases

## Slide 3: What is demand response (DR)?
Supply = Demand condition
  Energy balance e.g., hourly wholesale markets
  Power balance e.g., 5-minute redispatch control
  Frequency control e.g., SCADA (area control)
Conventional approach
  Supply follows demand
Smart grid approach
  Load asked/allowed to participate

## Slide 4: Demand response benefits
Active end-use loads
  Participate in operations
  Minimal consumer impact
Benefits to consumer
  Savings opportunity
  Support for renewables
Benefits to utility
  Peak load reduction
  Regulating services
  Emergency operations

## Slide 5: Dispatch of demand response
Effective demand response requires a control input
  Direct load control uses a boolean signal
  Indirect load control uses a continuous signal
Signals can be sent by utilities or DR aggregator
  Prices and/or other dispatch signals
  Optimal signals (e.g., lambda) are effectively prices
Markets can be used to “discover” prices
  Mechanism design problem
  Incentive compatibility
  Duality gap

## Slide 6: Market-based DR
Bids submitted by two primary resources
  Supply – bid power they can provide at a given price
  Demand – bid power they can forgo at a given price
  Both bids are for a finite time interval
Market closes and clears
  Bidding process is stopped
  Supply and demand bids are sorted to two curves
  Intersection of curves is the clearing price and quantity
Process repeated for every time interval

## Slide 7: Price Elasticity of the End Use Loads
Demand
(elastic)
Demand
Supply
Price
Quantity (MW)
Price ($/MW)
Price
(inelastic)
Notes: Changing today's inelastic demand to dynamically respond to the market is broadly recognized as the key to stabilizing prices … and allowing lead time to add capacity at lower risk.
The technology to create a much more elastic demand curve must move quickly into the market, and dynamic markets for supply and demand must be created on many levels and scales.

## Slide 8: Impact of inelastic demand
Systems design to meet peak inelastic load
  Requires more installed generation capacity
  Causes more costly unit to be dispatched on peal

## Slide 9: Utilization of Electricity Infrastructure
25% of distribution & 10% of generation assets
  Asset value is 100s of billions of dollars used less than 400 h/y
  Similar for transmission
5%
5% = ~400 hrs/yr
75%
90%
Hourly Loads as Fraction of Peak, Sorted from Highest to Lowest
(8,760 hrs)
distribution
generation
Notes: Grid assets must be sized to meet peak demand, but their overall utilization over the course of the year is low.
These are load duration curves in which the loads for the year (hourly in this case) are sorted from highest to lowest.
When normalized to the peak load (100% load factor), they illustrate the utilization of an asset.
This plot shows the utilization of generation and a typical distribution feeder in the U.S.
Note that the average utilization (50-th percentile) for the year for generation is about 70%.
For distribution it is below 50%.
These do not include the reserve margins, which lower utilization of actual capacity substantially.
(CLICK) Note how much capacity is needed for only 5% of the hours of the year (438 hours):
(CLICK) 25% of our distribution capacity
(CLICK) and about 10% of our generation capacity exist only to serve loads for those few hours.
If we can displace those loads with demand response, distributed generation, and efficiency measures …
That would represent huge reductions in needed infrastructure.

## Slide 10: Peak Load Reduction
Non-linear power system characteristics
  Variable efficiencies
  Higher losses under heavy loading
  Peak generating units are typically less efficient
High peak load conditions are more costly
  Reduces profit under most tariffs

## Slide 11: Peak Load Reduction cont.
Line Losses
Typical power line
  Quadratic losses
Generator Efficiencies
Heat Rate
  British Thermal Units (Btu) to generate 1 kWh electric energy
  Coal Steam: 10,818 Btu/kWh
  Combined Cycle: 8,931 Btu/kWh
  CT/Diesel: 11,667 Btu/kWh

## Slide 12: Optimal Peak Reduction
If generators "follow" load
  Must meet peak loading
If the load is “flattened”
  Same energy with less infrastructure
  Stay at optimal efficiency
How?
  Storage (expensive)
  Flexible loads (too few)

## Slide 13: Realistic Peak Reduction
Cannot completely flatten load
Focus highest peaks
  Greatest benefits (non-linear)
Utility priorities
  Efficiency programs (DSM)
  Behavior changes (Tariffs)
  Demand response

## Slide 14: Load-base regulating services
Loads always fluctuate
  Different frequency components
  Diversity effects
System adjusts to follow load
  Local voltage control
  System frequency regulation
Demand can provide regulation
  Frequency response (droop)
  Voltage response

## Slide 15: Emergency Conditions
Blackout are complex events
  Involves millions of components
  Heavy load often cited as contributing factor
  No feedback to customer when load is endangering a system
  Demand response can automate system protection

## Slide 16: What are we trying to do?
Managing an Actual Distribution Constraint from
the Olympic Peninsula Demonstration
Unless DG or storage are present, there is no safe way to serve overload!
feeder capacity

## Slide 17: How do we manage the response?
Initially AC = 0 (~20 min)
Rises to ~80% of initial load (~1 hr), ~93% at steady-state
Cooldown load at full capacity (~1/2 hr) – “rebound” effect
Ongoing cooldown to 125% of initial load (~1 hr)
The key challenge for DR is managing the rebound!

## Slide 18: What can GridLAB-D do?
11.5% load reduction on peak day
  Accomplished with complex system of rotating TOU prices

## Slide 19: What are the effects to the customer?
TOU/CPP homes provide ~2F average increase
  Duration of thermostat setup is 6 hours during peak
  Unintended consequence: high CPP prices lowered comfort

## Slide 20: Types of demand response
Direct load control
  Load control remote control switch
  Thermostat setback control
Indirect load control
  Time Of Use (TOU)
  Critical Peak Price (CPP)
  Real Time Price (RTP)
    Passive (single auction/no load bidding)
    Double Auction (load bidding)
Distributed Control (Grid Friendly Appliances)

## Slide 21: Direct Load Control
Utility has a direct control path to the appliance controller.
  Customer compliance obtained through tariff or contract
  Utility controls end use load according to tariff/contract.
  Customer compensated for allowing this type of control
  Additional compensated may be given for using the control
  Utilities like “big red button” can push when needed
  Know exactly how much load should respond
  Caveats: free-riders, active load fraction, equipment failures

## Slide 22: Time-of-use (TOU)
Implemented as a tariff or rate design
  Voluntary (op-in, opt-out)
  Mandatory (regulator-approved)
Two or more tiers
  Off-peak (low price)
  Shoulder (average price)
  On-peak (high price)
On-peak to off-peak ratio must be significant
  Low  increases customer costs  fewer customer signup

## Slide 23: TOU schedules
schedule cooling_setback {
16-21 * * * * 1; // peak-time setback
22-15 * * * * 0; // off-peak setback
}
object house {
cooling_setpoint cooling_setback*2+72;
}

## Slide 24: Critical Peak Pricing (CPP)
CPP can be implemented in 2 ways
Human response – e.g., phone call, email, text message
  Difficult to model
  More common approach
Hardware response – e.g., utility signal to appliances
  Easy to model
  Less common approach

## Slide 25: CPP signals
class house {
double price_signal[$/MWh];
double price_sensitivity[degF*MWh/$];
}
object house {
price_sensitivity 0.1;
cooling_setpoint cooling_offset*comfort+72;
object player {
file “cpp.csv”;
target price_signal;
};
}

## Slide 26: Demand Response Rebound
DR operates by adjusting power and/or energy demand
  Thermostatic have internal closed loop on energy
  DR relies on thermal mass to defer power demand
There is a limited resource
  HVAC system can defer operation but must eventually turn on
  Dryer can lower temperature, but energy to dry is fixed
  Resource magnitude depends on technical/social constaints
With a TOU or CPP a rebound can be experienced

## Slide 27: Demand response rebound

## Slide 28: Real Time Price (RTP)
A real time price is similar to a TOU price with a hardware implementation except that the price can change every 5 minutes.
Because it changes so often it is necessary to implement this with hardware.
A RTP is a more accurate representation of the true cost of consuming electrical energy.

## Slide 29: RTP prices
class house {
double price_signal[$/MWh];
double price_sensitivity[degF*MWh/$];
}
object house {
price_sensitivity 0.1;
cooling_setpoint cooling_offset*comfort+72;
object player {
file “rtp.csv”;
target price_signal;
};
}

## Slide 30: GridLAB-D Tutorial 4
Part 2: Real-time pricing markets

## Slide 31: Real time markets
RTP can include many different costs in a system
  Wholesale power cost
  Transmission level congestion cost
  Distribution level congestion cost
  Regulation cost
RTP signal can reveal true cost
  Consumer avoids complexity of power system
Note: signal may not be actual price
  Number which indicates relative cost at a given time

## Slide 32: RTP-Double Auction Market
Demand
(elastic)
Demand
Supply
Price
Quantity (MW)
Price ($/MW)
Price, mitigated
(inelastic)
Notes: Changing today's inelastic demand to dynamically respond to the market is broadly recognized as the key to stabilizing prices … and allowing lead time to add capacity at lower risk.
The technology to create a much more elastic demand curve must move quickly into the market, and dynamic markets for supply and demand must be created on many levels and scales.

## Slide 33: RTP-Double Auction Market
A double auction can mitigate rebound
A true double auction can address many issues
  Combined bids from loads, distributed generation and storage
Issues when market is “cleared”
  Equitable solutions (differences between feeder)
Double auction requires bids from participants
  More upstream than simple RTP system

## Slide 34: Market Clearing

## Slide 35: Market Objects
Controller
Auction
Passive Controller
Stub Auction
Note: Passive controller can be used with an auction, or a number of other objects.
Used for delivering prices to a purely reactive controller.
Used to create a two-way, transactive bidding market.

## Slide 36: Auction and Controller Objects
Auction Objects
  One auction per feeder
Auction collects bids
  Clears the market periodically
  Delivers cleared prices
  Controller objects read prices
Wholesale price
  Player inputs LMP
Players for TOU/CPP/RTP
Controller Objects
Controller for each bidding object, e.g.,
  HVAC Thermostat
  Hot water heater
  EV charger
Bid reveals price at which load state will change
  Bid include power

## Slide 37: Stubauction Object
object stubauction {
name Market_1;
period 300;
object player {
file Price.player;
property current_market.clearing_price;
};
object recorder {
property avg24,std24;
limit 2880;
interval 60;
file price_statistics.csv;
};
}
The auction is responsible for determining the clearing price.
In a stub-auction there is no clearing of the market, the clearing price is input through a .player file.

## Slide 38: Passive Controller – HVAC
k
Tmax
Tmin
k
Temperature
Price*
Tcurrent
Pavg
Pclear
Tset
Tdesired

## Slide 39: Passive Controller - HVAC
object passive_controller {
base_setpoint cooling3*1;
control_mode RAMP;
sensitivity 1;
expectation_obj Market_1;
expectation_prop avg24;
setpoint_prop cooling_setpoint;
state_prop override;
observation_obj Market_1;
observation_prop current_market.clearing_price;
mean_observation_prop avg24;
stdev_observation_prop std24;
range_low -1.500;
range_high 2.500;
ramp_low 1.333;
ramp_high 0.800;
}
The passive controller does not send a bid signal to the market.
This implies unidirectional communications.
This controller is set for a 24 hour moving window for market values.
The moving window can be changed to any value.
Ramp and Range values set the “responsiveness” of the passive controller.

## Slide 40: Price Player
2000-01-01 00:00:00,0.065139609
+1h,0.063279907
+1h,0.047926635
+1h,0.054980748
+1h,0.054144897
+1h,0.052692165
+1h,0.025675894
+1h,0.048756545
+1h,0.060731834
+1h,0.067444366
+1h,0.077139106
+1h,0.115129386
+1h,0.314471806
+1h,0.103280668
+1h,0.107517265
+1h,0.090978092
+1h,0.099465131
+1h,0.163445608
+1h,0.188779549
+1h,0.122554232
+1h,0.281734869
+1h,0.240559158
+1h,0.082833806
+1h,0.081005661
+1h,0.062340608
+1h,0.058395271
The price.player file reads a price into the auction object.
This price is used to represent the cleared price of power for a TOU or RTP market structure.
The example shows price in 1 hour time steps, but smaller or larger time steps can be used.
A price signal is then sent to every control and based on this signal and the controller values.
The load will then respond accordingly.

## Slide 41: Population Statistics
HVAC units in one of 4 modes.
  Off
  Cooling
  Heating
  Heating (AUX)
Control signals distort population statistics.
Multi-state physical models
  Simulates how the control signal affect population
  Changes power consumption

## Slide 42: DLC in GridLAB-D
HVACs - Cycling
object passive_controller {
control_mode DIRECT_LOAD_CONTROL;
dlc_mode CYCLING;
cycle_length_on 803;
cycle_length_off 917;
state_property override;
observation_object Market_1;
observation_property past_market.clearing_price;
second_tier_price 0.680986;
};
object passive_controller {
period 900;
control_mode PROBABILITY_OFF;
distribution_type NORMAL;
observation_object Market_1;
observation_property past_market.clearing_price;
stdev_observation_property my_std;
expectation_object Market_1;
expectation_property my_avg;
comfort_level 9999.00;
state_property override;
};
Water Heaters - Probabilistic
object passive_controller {
control_mode DIRECT_LOAD_CONTROL;
dlc_mode OFF;
state_property override;
observation_object Market_1;
observation_property past_market.clearing_price;
second_tier_price 0.680986;
};
Pool Pumps - Off

## Slide 43: Price Elasticity
Represent change in load from change in price
  Used for loads that don’t automate DR controls (e.g. dryers).
Based on PRISM1 models.
  Empirically based – data needed from DR studies
1A. Faruqui and L. Wood, “Quantifying the Benefits of Dynamic Pricing in the Mass Market”, The Brattle Group, Prepared for Edison Electric Institute, January 2008.

## Slide 44: Price Elasticity Model
Substitution Elasticity
  Customer’s willingness to shift their energy usage from on-peak to off-peak time periods (deferred energy usage).

## Slide 45: Price Elasticity Model (cont.)
Daily Elasticity
  Customer’s willingness to decrease (or increase) daily energy consumption in response to a change in price.

## Slide 46: Elasticity in GridLAB-D
object passive_controller {
period 900;
control_mode ELASTICITY_MODEL;
two_tier_cpp true;
observation_object Market_1;
observation_property past_market.clearing_price;
state_property multiplier;
linearize_elasticity true;
critical_day CPP_days_R1.value;
first_tier_hours 12;
second_tier_hours 12;
third_tier_hours 6;
first_tier_price 0.069987;
second_tier_price 0.139973;
third_tier_price 0.699867;
old_first_tier_price 0.124300;
old_second_tier_price 0.124300;
old_third_tier_price 0.124300;
daily_elasticity -0.1305;
sub_elasticity_first_second -0.0198;
sub_elasticity_first_third -0.0290;
}
The passive controller does not send a bid signal to the market, as it is representing human behavior (child of a ZIPload).
Can represent either 2-rate or 3-rate plus CPP.
Each rate period has it’s own elasticity in comparison to lowest rate period.
Negative elasticity represents less energy consumption (daily) and less energy consumed during critical period (substitution).
Updates percent load change every market period.

## Slide 47: Auction Objects
object auction { string name; string unit; //i.e. MW, kW, or kWh integer period[s]; // Interval between market clearings
integer latency[s]; // Lag between clearing and delivery
string special_mode; // Allows for buyer or seller only
double pricecap; // Maximum bid price allowed
boolean verbose; // Allows user to watch bidding
double init_price; // Used to “bootstrap” market if warmup=TRUE
double init_stdev;
object capacity_reference_object; // more details following
integer warmup; // 1=TRUE, 0=FALSE
}
Defines market intervals
  Provides clearing price and quantity after clearing, average prices, and standard deviation
  Allows for active bidding from buyers and sellers
  Also available – previous and current market clearing statistics such as marginal quantity, marginal load, etc.

## Slide 48: Auction Objects
The statistical interval desired must be created by the user in the following form:
  class auction {
  double yyyy_price_mean_xx;
  double yyyy_price_stdev_xx;
  }
Where “yyyy” can be “current” or “past” and “xx” can be “#m”, “#h”, “#d”, or “#w”:
  class auction {
  double past_price_mean_5d;
  double current_price_stdev_3m;
  }
Any number of statistics can be created and used by various objects

## Slide 49: Auction Objects
Available auction outputs:
  user specified statistics
  current_market.clearing_price
  current_market.clearing_quantity
  past_market.clearing_price
  past_market.clearing_quantity
  clearing case type

## Slide 50: Capacity Object
Acts as a supply agent
  limits power flowing through object (or other properties)
  If below capacity, market should clear at bid price
  If at/above capacity, should clear to limit quantity
Unresponsive load
Responsive or bidding load
Load bid
Seller bid
to pricecap
Seller bid is a user-defined quantity and typically an RTP price signal
Buyer bid is the estimate of the unresponsive load as the quantity and price cap

## Slide 51: Example Capacity Object
object auction {
name Market_1;
type DOUBLE;
unit kW;
period 300;
// Initial statistics to stabilize initial market
init_price 35.0001;
init_stdev 10;
warmup 1;
// looking at the feeder regulator and power flowing through
capacity_reference_object 1406_regulator;
capacity_reference_property power_out_real;
capacity_reference_bid_price seller1*1;
max_capacity_reference_bid_quantity 125; //kW
}

## Slide 52: Bidding Function
When auction is established objects can submit bids
  submit_bid function structure
  Market to bid into
  Object that is bidding
  Quantity to bid
  Price of bid

## Slide 53: Clearing of the Market
  Previous values stored in past_market.clearing_price and past_market.clearing_quantity
  Current cleared values stored in current_market.clearing_price and current_market.clearing_quantity
  Output values can be read by recorder - or – directly delivered to a controller object

## Slide 54: Controller Objects
Provides an interaction point between loads and market.
  Uses various external inputs to determine a bid_quantity and bid_price for the object it is attached to.
class controller { enumeration control_mode; // RAMP or DOUBLE_RAMP
string market; // Name of auction object to be used string parent; // Object modified by controller
string setpoint; // Set point to be modified by controller
string base_setpoint; // Desired set point value
string target; // Value set point is compared against integer period[s];
string demand; // Bid quantity of object
boolean verbose;
string bid_mode;
string simple_mode; // Various “easy” connections to appliances
property average_target;
property standard_deviation_target;
…
}

## Slide 55: Controller Objects - Ramp
object controller { …
control_mode RAMP;
double range_low;
double range_high;
double ramp_low;
double ramp_high;
double slider_setting_heat; //Simple pre-set slider 0-100%
double slider_setting_cool; //participation in market (DOUBLE_RAMP)
double slider_setting; //(RAMP) – sets ranges and ramps
}
Control mode dependent on object being controlled
  Determines how object bids and responds to price
  RAMP and DOUBLE_RAMP modes control thermostatic set points

## Slide 56: Controller Objects - Ramp

## Slide 57: Controller Objects – Double Ramp
Normal action could cause conflicting pre-cooling and pre-heating states
DOUBLE_RAMP provides two means for resolving this conflict (deadband and sliding)

## Slide 58: Controller Objects – Double Ramp
deadband resolution essentially limits the range of the pre-cooling and pre-heating and determines an average amount.
sliding resolution determines which mode (heat or cool) was last used, and allows this to override the other.

## Slide 59: Controller Objects
object passive_controller { string control_mode; //RAMP, PROBABILITY_OFF, others TBD
string mean_observation_property;
string stdev_observation_property;
string expectation_object;
string expectation_property;
string observation_object;
string observation_property; string parent;
string setpoint;
string base_setpoint;
string setpoint_property;
string state_property; integer period[s];
enum distribution_type; //NORMAL, UNIFORM, EXPONENTIAL (PROB_OFF)
double comfort_level; //0-inf (PROB_OFF)
double range_low/high, ramp_low/high; //(RAMP)
}
Responds to a signal (not just price), but does not bid into market.

## Slide 60: Example controllers
object controller {
market Market_1;
bid_mode ON;
control_mode DOUBLE_RAMP;
resolve_mode DEADBAND;
slider_setting_heat 0.500;
slider_setting_cool 0.500;
heating_base_setpoint 68;
cooling_base_setpoint 74;
period 300;
average_target current_price_mean_24h;
standard_deviation_target current_price_stdev_24h;
target air_temperature;
heating_setpoint heating_setpoint;
heating_demand last_heating_load;
cooling_setpoint cooling_setpoint;
cooling_demand last_cooling_load;
deadband thermostat_deadband;
total hvac_load;
load hvac_load;
state power_state;
};
object passive_controller {
period 300;
control_mode PROBABILITY_OFF;
distribution_type NORMAL;
observation_object Market_1;
observation_property current_market.clearing_price;
stdev_observation_property current_price_stdev_24h;
expectation_object Market_1;
expectation_property current_price_mean_24h;
comfort_level 1.00;
state_property override;
};
object controller {
market Market_1;
bid_mode ON;
control_mode RAMP;
slider_setting 0.500;
base_setpoint cooling7*1;
period 300;
average_target current_price_mean_24h;
standard_deviation_target current_price_stdev_24h;
target air_temperature;
setpoint cooling_setpoint;
demand last_cooling_load;
total hvac_load;
load hvac_load;
state power_state;
range_high 5;
range_low -3;
};

## Slide 61: Customer Billing
Use triplex_meter (customer meter)
  Three billing types: UNIFORM, TIERED, HOURLY (RTP)
  Includes a monthly fee and bill processing day
  bill_dump allows you to collect all bills in a single file
object triplex_meter {
bill_mode UNIFORM;
price 0.1; // $/kWh
bill_day 1;
monthly_fee 10; //$
}
object triplex_meter {
bill_mode TIERED;
price 0.1;
bill_day 1;
monthly_fee 10;
first_tier_energy 100;
first_tier_price 0.15;
second_tier_energy 500;
second_tier_price 0.18;
third_tier_energy 1000;
third_tier_price 0.20;
}
object triplex_meter {
bill_mode HOURLY;
// name of the auction
power_market my_market;
bill_day 1;
monthly_fee 10;
}
object bill_dump {
runtime ‘2000-01-01 00:00:00’;
filename my_bill_dump.csv;
}

## Slide 62: GridLAB-D Tutorial 4
Database operations

## Slide 63: Module globals
Implements same functionality as tape module
Global variables for mysql module:
  module mysql {
  hostname "localhost";
  username "gridlabd";
  password "";
  schema "gridlabd";
  port 3306;
  socketname "/tmp/mysql.sock";
  }

## Slide 64: Database object
Used by other objects to make queries
  Specify server access/protocol
  Specify default behaviors and options
Multiple database objects allowed
  If multiple used, each object must specify database to use
Options:
  NOCREATE: disables automatic table creation
  NEWDB: destroys old schema before starting simulation
  OVERWRITE: destroys old data before writing new data

## Slide 65: Database object properties
  object database {
  hostname "localhost";
  username "gridlabd";
  password "";
  schema "gridlabd";
  port 3306;
  socketname "/tmp/mysql.sock";
  options SHOWQUERY|NOCREATE|NEWDB|OVERWRITE;
  on_init file-name;
  on_sync file-name;
  on_term file-name;
  sync_interval seconds;
  tz_offset seconds;
  uses_dst FALSE;
  }

## Slide 66: Players
object player {
property property-name;
table source-table;
connection database-object-name;
loop number-of-loops;
}
Syntax compatible with tape:player
  “file”  “table”
  “mode” and “filetype” are ignored

## Slide 67: Recorders
Target object is parent (if specified)
  If absent, all properties my use specify object name
Table name (aka, “file”)
  Multiple objects can use same table (must have same fields)
Property list
  Multiple fields allowed (comma separated)
  Object name allowed (e.g., “name.property”)
Special fields
  Record id, default is “id”
  Timestamp, default “t”
  Header fields (name, class, latitude, longitude), default is “”

## Slide 68: Collectors
object collector {
property property-name;
group group-spec;
table|file source-table;
mode {"w","w+","a","a+"};
limit max-rows;
interval seconds;
connection database-object-name;
options PURGE;
}

## Slide 69: MySQL Workbench

## Slide 70: Exercises

## Slide 71: Exercises
Run the CVR 13 Node system for 7 days with a constant price signal.
Plot the Regulator apparent power consumption, voltage at the regulator control node, price signals, and the HVAC system population statistics.
What is the peak load and how many HVAC units are in operation at this time?

## Slide 72: Exercises
Run the CVR 13 Node system for 7 days with the default price signal.
Plot the Regulator apparent power consumption, voltage at the regulator control node, price signals, and the HVAC system population statistics.
How does the system operate with the price signal compare to without?

## Slide 73: Exercises
Develop a control signal, i.e. price signal, that you think optimally controls the system. Explain your basis for this control signal.
Run the CVR 13 Node system for 7 days with the custom price signal.
Plot the Regulator apparent power consumption, voltage at the regulator control node, and the HVAC system population statistics.
How does this signal perform.
What is your opinion of a passive control signal?

## Slide 74: Exercises
Using the IEEE 4-node, replace the load with a single home (don’t forget the transformer) with a double ramp HVAC controller.
  Create an auction object using 24 hour statistics in BUYER_ONLY mode.
  Observe the difference in demand when using different slider settings.
Add a water heater and a passive controller in probabilistic off mode. Observe the effect of the comfort level on demand.
Add billing to the customer meter and try the various billing types. Observe the differences in bills.
Observe the IEEE-13 node test system with markets.